## Slide 1
HVAC Certification, Tools and Training

## Slide 2: EPA Requirements
Ozone damaging refrigerants was agreed to be phased out at the Montreal Protocol in 1987
In 1992, a time line was established and certification required
Two categories of air conditioning systems was created – 608 and 609
Can not vent refrigerant to atmosphere
Must use EPA Approved equipment
Equipment must be registered with your regional EPA office

## Slide 3: Fines for Violation

## Slide 4: 608 or 609
609 controls mobile air conditioning systems
608 controls stationary air conditioning systems
Unfortunately, it is not quite that simple

## Slide 5: EPA Classifications

## Slide 6: EPA 608 Requirements

## Slide 7: EPA 609 Requirements

## Slide 8: EPA 609 Technician Certification
Can be completed on line or as a mail in test
Open book test
Lifetime certification
Primarily designed for mobile air conditioning systems
Test costs @$20 per person

## Slide 9: EPA 608 Technician Certification
Must be conducted by certified proctored
Closed book test
Lifetime certification
Core Knowledge required for all types
  Type I – Small Appliances
  Type II – Residential Systems
  Type III – Low Pressure Vapor Systems
  Universal – All Systems
Cost @$75 and up

## Slide 10: Refrigerant Purchasing
January 2018 requires only certified technicians to be able to purchase refrigerant (H134a now)
Must be able to prove your company has at least one technician is certified
Larger volumes may require proof of 608 certification
Best Practice – Track purchases and usage

## Slide 11: Current Refrigerants

## Slide 12: Are You Using the Right Equipment?

## Slide 13: All in One Machines
Designed for automotive systems
Slow to evacuate
OK for recycling
Make sure you have extra tanks

## Slide 14: Appion G5 Twin Recovery Machine
Designed for commercial refrigeration
Can remove up to 6 pounds of refrigerant per minute
Costs @$750

## Slide 15: Vacuum Pump
6 to 7 cfm
Oil must be changed every job
Use vacuum pump oil and not POE oil

## Slide 16: Manifold Gauges
Must be kept sealed when not in use
Easily knocked out of calibration
Not accurate for evacuation

## Slide 17: Micron Gauge
Much more accurate than a Manifold Gauge needle
1 inch of mercury on a Manifold Gauge equals 25,000 microns
Systems must be evacuated to 750 to 1000 microns
A must have to properly service HVAC systems

## Slide 18: Are You Servicing Your Equipment Correctly?
Changing filters as required by the equipment manufacturer
Changing oil as required by equipment manufacturer
Leak testing manifold gauges and hoses

## Slide 19: Refrigerant Quality
What are you putting back in?
Has it been fully recycled?
Is it mixed with other refrigerant?
Does it contain non condensable gas (nitrogen and air)?

## Slide 20: Training

## Slide 21: Proper Training
Where was training on HVAC systems completed?
How long was the training?
Was HVAC experience learned just from others?

## Slide 22: What We Have Seen
Very little formal training
Training on automotive and truck systems only
Knowledge gained through trial and error
Knowledge gained from others who learned on their own

## Slide 23: Normal OEM Training
Training on system used
Assumes solid HVAC knowledge already exists
Normally 2 to 3 days
You can not learn HVAC in this short of time

## Slide 25: MCI Academy
Developed a HVAC Specialist program
4 weeks in length – not consecutive weeks
  HVAC 101 – 3.5 days – Fundamentals and EPA Certification
  HVAC 201 – 4.5 days – Major Components
  HVAC 301 – 4.5 days - Service
  HVAC 401 – 4.5 days – Troubleshooting

## Slide 26: System Qualifications
LMS Courses, Classroom Sessions, Practical and Written Testing
16 different qualifications available

## Slide 27: Qualifications Lead to Certificates
Technician Level 3
Preventive Maintenance Qualification
Tires and Wheels Qualification
MCI Air Systems Qualification
MCI Basic Steering Systems Qualification
MCI Basic Suspension Systems Qualification
Tire Pressure Monitoring Systems Qualification
Technician Level 2
Drum Brakes Qualification
Disc Brakes Qualification
Wheel End Systems Qualification
Antilock Brake Systems Qualification
MCI Basic Electrical Qualification
MCI Advanced Steering Systems Qualification
MCI Advanced Suspension Systems Qualification
Auxiliary Heating Systems Qualification
Technician Level 1
MCI HVAC Qualification
Advanced Electrical Systems Qualification

## Slide 28
MCI Technician Level 3
MCI Technician Level 2
MCI Technician Level 1
MCI HVAC Specialist Diploma
Electrical Specialist Diploma
Master MCI Technician
C
A
R
E
E
R
or
and

## Slide 29: Graduate Recognition

## Slide 30
Motorcoach Technician Apprenticeship Program
Notes: Welcome to the MCI Academy On line training library. The topic you have selected is Emergency Evacuation Guidelines. These Guidelines are only general in nature because each situation may require different responses.

## Slide 31: Summary of Credentials to be Earned
(16) System Qualifications
(3) Technician Level Certificates
Commercial Driver’s License
(2) Specialist Diplomas
EPA 608 and 609 certifications
Master MCI Technician certificate
Motorcoach Technician Journeyman certificate